## Slide 1: VoiceFilter-Lite: Streaming Targeted Voice Separation for On-Device Speech Recognition
Authors: Quan Wang, Ignacio Lopez Moreno, Mert Saglam, Kevin Wilson, Alan Chiao,
Renjie Liu, Yanzhang He, Wei Li, Jason Pelecanos, Marily Nika, Alexander Gruenstein
Presented by: Quan Wang <quanw@google.com>
Notes: Paper: https://arxiv.org/abs/1710.10467

## Slide 2: Key messages
What:
  A single-channel source separation model for a target speaker
  Part of on-device streaming ASR
Why:
  Improve ASR on overlapped speech drastically
How:
  Filterbanks as inputs and outputs
  Asymmetric loss and adaptive runtime suppression strength
  Quantize to 8-bit integer model

## Slide 3: Part 1: Recap of VoiceFilter

## Slide 4: The Cocktail Party Problem
The problem:
Multiple talkers speaking simultaneously
You just want to listen to one person
Conventional solutions:
Multi-channel blind separation
Single-channel blind separation
Image from elixirofknowledge.com
Image from Nima Mesgarani, Columbia University
Notes: The problem we are solving is known as the cocktail party problem.
When multiple talkers are speaking, and you only want to listen to one person, that's easy for human but difficult for machines.
If there are multiple channels, like human has two ears, multi-channel blind separation algorithms can be used.
But many devices like mobile phones only have one microphone, then single-channel blind separation algorithms can be used.

## Slide 5: Knowing “whom to listen to”
Voice Match already deployed to:
  Android smart phones
  Smart home speakers
User’s voice profile stored on device
Blindness sucks
  Number of sources is unknown
    Single: don’t want to mess up
    Multiple: only keep target voice
  Multiple outputs, still don’t know which one to use (e.g. to run ASR)
    Pick loudest?
    Run speaker verification on all?
  Permutation invariance: computational cost is high!
Notes: For example, if you have an Android Phone or Google Home device, you can enable VoiceMatch, which will store a voice profile on the device.
With this voice profile, we are no longer blind.
Here I will explain why blindness sucks.
First, in blind separation, you don't know how many sources are there in the runtime. You may be doing great when the input has multiple sources, but you also don't want to mess up when the input is already single source.
Second, blind separation usually has multiple outputs, you still need to pick the one you need, for example to run ASR.
You can simply pick the loudest one from the outputs, or use an additional speaker verification step, but it's not a trivial task itself.
Finally, permutation invariant training is usually very expensive.

## Slide 6: VoiceFilter: Say Goodbye to blindness!
Condition the voice separation task by target speaker embedding
Blind separation
Noisy multi-speaker audio
Clean audio of target speaker
Target speaker embedding
VoiceFilter
Notes: So, with the proposed VoiceFilter system, we can say Goodbye to blindness.
We make use of the speaker embedding, which can be acquired during user enrollment. This speaker embedding will condition the separation system to output the clean signals from the target speaker.

## Slide 7: Learn more about VoiceFilter
https://www.youtube.com/watch?v=gnRX2lzepz0

## Slide 8: Part 2: VoiceFilter for on-device ASR

## Slide 9: On-device ASR
Moving ASR from cloud to device is the trend
  No requirement for Internet
  Much less latency due to communications
  Better privacy preservation
Example use cases (smartphones, smart home devices):
  “Turn on flashlight”
  “Turn on bedroom lights”

## Slide 10: Challenges: On-device VoiceFilter
Memory and storage:
  Model should be really tiny (few MB, not GB)
CPU and battery:
  Less runtime operations
Latency:
  Model should work in a streaming fashion
  ASR should never wait for VoiceFilter

## Slide 11: Challenges: VoiceFilter for ASR
Quality:
VoiceFilter: You either always run it, or never run it
Being
always harmless
is more important than being
sometimes helpful!
Clean single speaker
Non-speech noise
Reverberant rooms
Different SNR

## Slide 12: Part 3: The journey to Lite

## Slide 13: Optimizing for CPU and latency
CNN layer
Time-frequency CNN
  Temporal CNN: Not causal
  Convolutions: Computationally expensive
freq
time
Receptive field can’t see the future

## Slide 14: Optimizing for CPU and latency
LSTM layer
LSTM layer
Bi-directional LSTM
  Backward pass: Not causal
time
We can't use backward LSTM

## Slide 15: Optimizing for CPU and latency
If we only care about ASR:
  ASR inputs directly as VoiceFilter inputs & outputs
  No need to convert back to waveform
  No cool audio demos
spectrogram
Neural Network
spectrogram
spectrogram
filterbanks
Speech Recognition
d-vector
STFT
iSTFT
STFT
VoiceFilter
system
Redundant

## Slide 16: Let’s simplify the feature frontend
ASR uses stacked log Mel-filterbanks as input

## Slide 17: Model architecture
Assume we use stacked filterbanks as VoiceFilter-Lite I/O

## Slide 18: What have changed since VoiceFilter
 | VoiceFilter | VoiceFilter-Lite
Input & Output | Audio waveform | ASR features (FFT magnitude, filterbank, etc.)
Inference | Full sequence offline inference | Online streaming inference (no time-freq CNN, no bi-LSTM)
STFT and iSTFT | Part of VoiceFilter model graph | STFT as part of ASR system; no iSTFT
Model format and size | TensorFlow graph; typically >100MB | Quantized to int8 TFLite model; typically <10MB

## Slide 19: VoiceFilter-Lite vs joint training with ASR
Joint training with ASR
  Concatenate d-vector with filterbanks for ASR training
  Creates dependency between ASR and speaker recognition models
  What if user did not enroll (d-vector not available)?
VoiceFilter-Lite
  It’s a plug-and-play model
  ASR can be retrained and replaced independently
  Can be simply disabled by passing through the inputs
filterbanks
ASR
d-vector
Concat

## Slide 20: Part 4: The long fight with over-suppression

## Slide 21: Why it’s a hard problem
Modern ASR models are already noise-robust
  Multistyle training (MTR)
  SpecAugment
Further masking the input of such a model is risky
  Early experiments show that adding VoiceFilter-Lite model will:
    Reduce WER on speech noise cases
    Increase WER on clean cases and non-speech noise cases
      Most errors in WER are deletion errors – over-suppression

## Slide 22: Asymmetric loss
Less tolerant to over-suppression, and more tolerant to under-suppression
  Conventional reconstruction L2 loss:
  Asymmetric L2 loss, with over-suppression penalty :
clean
spectrogram
enhanced
spectrogram

## Slide 23: Adaptive suppression strength
We use a weight to control suppression strength
We want the weight to be:
  Larger – when there is overlapped speech (VoiceFilter-Lite is most helpful)
  Smaller – when the speech is clean, or contains only non-speech noise (VoiceFilter-Lite could be harmful)

## Slide 24: Adaptive suppression strength
We add a side output to the model, and a prediction loss to the total loss

## Slide 25: Adaptive suppression strength
Denote this noise type prediction as
  0 – clean speech, or containing non-speech noise
  1 – overlapped speech
Adaptive suppression strength:
  – moving average
  – linear transform

## Slide 26: Part 5: Experiment setup

## Slide 27: Metrics
Word Error Rate (WER) is all we need
Why not signal-to-noise ratio (SNR) or source-to-distortion ratio (SDR)?
  There is no audio
  The I/O of VoiceFilter-Lite are ASR features

## Slide 28: Models
Speaker recognition (enrollment):
3 LSTM layers, each with 768 nodes and 256-dim projection
1 final feedforward layer with 256 nodes
VoiceFilter-Lite:
3 LSTM layers, each with 512 nodes
1 feedforward layer with sigmoid activation for mask prediction (dimension depends on I/O)
2 feedforward layers, each with 64 nodes for noise type prediction

## Slide 29: Data generation for training and evaluation
Clean speech
Room configurations
Non-speech noise
Interfering speech
Room simulator
SNR 1dB~10dB
Room simulator
SNR 1dB~10dB
Non-speech noise additive
Non-speech noise reverberant
Speech additive
Speech noise reverberant
(case 1)
(case 2)
(case 3)
(case 4)
(case 5)
SNR 1dB~10dB
SNR 1dB~10dB
Music
Sound effects
Cafe ambient noise
Car ambient noise
Quiet ambient noise

## Slide 30: Two experiment groups
Group 1: LibriSpeech
RNN-T streaming ASR model trained on LibriSpeech training set
VoiceFilter-Lite also trained on LibriSpeech
Evaluate on LibriSpeech testing set (“test-clean” and “test-other”)
Group 2: Realistic speech queries
RNN-T streaming ASR model trained on YouTube, anonymized voice search, etc.
VoiceFilter-Lite training and ASR evaluation: Vendor collected dataset of realistic speech queries
Much more challenging than Group 1:
  More variations of prosody, sentiment, accent, and acoustic condition
  Domain mismatch with ASR training set

## Slide 31: Part 6: Results and conclusions

## Slide 32: Results of Group 1 (LibriSpeech)
VoiceFilter-Lite consistently improves WER on both non-speech noise and speech noise cases

## Slide 33: Results of Group 1 (LibriSpeech)
L2 loss: WER degrades on clean cases

## Slide 34: Results of Group 1 (LibriSpeech)
Asymmetric L2 loss: Less degradation on clean; also less improvement on speech noise cases

## Slide 35: Results of Group 1 (LibriSpeech)
Filterbank and stacked filterbank outperform FFT magnitude

## Slide 36: Results of Group 2 (Realistic speech queries)
L2 and asymmetric L2 loss: WER may degrade on both clean and non-speech noise cases

## Slide 37: Results of Group 2 (Realistic speech queries)
Lower suppression strength () – Tradeoff between:
  Degradation on clean or non-speech noise
  Improvement on speech noise

## Slide 38: Results of Group 2 (Realistic speech queries)
Adaptive suppression strength:
  Minimal degradation on clean or non-speech noise
  Still big improvement on speech noise
  Smaller model works similarly well

## Slide 39: Results of Group 2 (Realistic speech queries)
Can the model size go further down?
No voice filtering baseline:
  Speech noise, Additive: 56.5%
  Speech noise, Reverb: 53.8%

## Slide 40: Which frontend to use?
Filterbank and stacked filterbank outperform FFT magnitude
We prefer stacked filterbank over filterbank
  More context information
  Less runtime operations (usually subsample the frames after stacking)

## Slide 41: Conclusions
VoiceFilter-Lite: Use your enrolled voice to improve ASR on overlapped speech
It’s tiny, fast, streaming, and part of on-device ASR
Two approaches to resolve over-suppression issues:
  Asymmetric loss
  Adaptive suppression strength
A model of 2.2 MB:
  No WER degradation on clean and non-speech noise conditions
  25.1% (44.4% rel.) WER improvement on overlapped speech

## Slide 42: Demo

## Slide 43: Acknowledgement
We’d like to thank Philip Chao, Sinan Akay, John Han, Stephen Wu, Yiteng Huang, Jaclyn Konzelmann and Nino Tasca for the support and helpful discussions

## Slide 44: Questions?